| Department Details |
| --- |
| Location of Task: |  | Contact name and number: |  |
| Activity Description: | Entry into a confined space |
| Referenced SWMS: | SWMS 01; SWMS 02; SWMS 04; SWMS 05 |
| Plant and Equipment Involved: |  |
| PPE Required: (Tick as relevant) | Hard Hat | ( | Safety glasses / goggles | ( | Hearing Protection | ( | Fall Arrest Harness | ( | Other: | ( |
|  | Safety Boots | ( | Face Shield | ( | Gloves | ( | Respirator <Insert Type> | ( | Hi Vis shirt/vest | ( |
| Maintenance / Prestart Checks Required: | Completion of Confined Space Entry Permit & Risk Assessment |
| Certificates of Competency Required: | Certificate of Training in Confined Space Entry (in accordance with AS/NZS 2865) |
| Training / Competencies Required: | Induction into this Safe Work Method Statement |
| Occupational Health, Safety or Environmental Legislation: | Occupational Health and Safety Act 1984 (WA) Occupational Health and Safety Regulations 1996 (WA) | Codes or Standards Applicable to the Works: | Confined Spaces – Code of Practice 2011 AS/NZS 2865 – Safe Working in a Confined Space AS 1319 - Safety signs for the occupational environment |

# Risk Matrix

| Perform a risk assessment for each hazard identified by: (i) Determining the consequences (refer Table 1); (ii) Determining the probability of the event occurring (refer Table 2); (iii) Apply the values obtained from Tables 1 & 2 to the Qualitative Risk Matrix (Table 3) to obtain the resultant Risk Score and Level. |
| --- |
| Table 1 – Consequence |  |
| Level Rating ASSESSMENT CRITERIA Injury or Disease Financial Loss (% of operational budget) Operational Efficiency Compliance Information and Evidence Reputation and Image 1 Insignificant No injuries or health effects Up to 0.025% Delay (up to 2 hours) in performance. All business objectives still achieved. Guidance required for compliance. Loss, unauthorised release or access to information resulting in an insignificant impact on operations and/or systems. Unsubstantiated Low impact Low or no media profile 2 Minor First aid treatment 0.025% - 0.15% Delay (2 hours – 1 day) in performance limiting full achievement of business objectives. Some minor, non-compliance issues. Loss, unauthorised release or access to information resulting in minor compromise of operations and/or systems. Substantiated Low impact Low media profile 3 Moderate Medical treatment 0.15% - 2% Delay (1 day – 1 week) in achievement of business objectives. Compliance or probity infringements. Loss, unauthorised release or access to information resulting in significant compromise of operations and/or systems. Substantiated Public embarrassment Moderate impact Moderate media profile 4 Major Permanent disability or disease 2% - 6% Delay (1 week – 1 month) with potential for non-achievement of major business objectives. Non-compliance resulting in penalties. Loss, unauthorised release or access to information resulting in substantial compromise of operations and/or systems. Substantiated Public embarrassment High impact High media profile Third party action 5 Catastrophic Death > 6% Delay >1 month. Non-achievement of major business objectives. Non-compliance resulting in criminal charges or loss of accreditation. Loss, unauthorised release or access to information resulting in the cancellation of an operation(s) and/ or total compromise of systems. Substantiated Public embarrassment Very high multiple impacts High widespread media profile Third party action Table 2 - Likelihood Level Descriptor Description Frequency 1 Rare The event may occur in exceptional circumstances. Has the event occurred during the last ten years? Is there more than a 5% chance of the event occurring? 2 Unlikely The event could occur at some time. Has the event occurred during the last five years? Is there more than a 10% chance of the event occurring? 3 Possible The event should occur at some time. If the event has occurred during the last five years has it occurred more than once? Is there more than a 25% chance of the event occurring? 4 Likely The event will probably occur in most circumstances. Has the event occurred during the past year? Is there more than a 50% chance of the event occurring? 5 Almost Certain The event is expected to occur in most circumstances. If the event has occurred during the past year has it occurred more than once? Is there more than a 95% chance of the event occurring? |  |
| Table 3 – Risk Level Consequence Likelihood 1 2 3 4 5 Rare Unlikely Possible Likely Almost Certain 1 Insignificant 1 2 3 4 5 2 Minor 2 4 6 8 10 3 Moderate 3 6 9 12 15 4 Major 4 8 12 16 20 5 Catastrophic 5 10 15 20 25 Table 4 - Level of Risk - Descriptor Low Risk Moderate Risk High Risk Critical Risk 1 - 4 5 - 8 9 -12 15 - 25 Table 5 - Control Rating Table Level Descriptor Description Detail E Excellent Doing more than what is reasonable under the circumstances. Controls fully in place and subject to continuous maintenance and monitoring. Protection systems are in place and continuously reviewed. Procedures are in place and regularly tested and reviewed. A Adequate Doing what is reasonable under the circumstances. Controls are in place and subject to periodic maintenance and monitoring. Protection systems are in place and are periodically reviewed. Procedures exist for given circumstances and are periodically tested and reviewed. I Inadequate Not doing some or all of the things that would be reasonable under the circumstances. Little or no action being taken. No protection systems exist or they have not been reviewed for some time. No formalised procedures exist. | Legend E: extreme risk; immediate reaction required (18-25) H: high risk; senior management attention needed (10-17) M: moderate risk; management responsibility must be specified (6-9) L: low risk; manage by routine procedures (1-5) |

# Table 6 - Risk Acceptance Table

| Level of Risk | Criteria for Acceptance of Risk | Authorised to accept |
| --- | --- | --- |
| Low | Acceptable | Acceptable with adequate controls | Risk Owner |
| Moderate | Acceptable with Monitoring | Acceptable with adequate controls | Manager |
| High | Acceptable with Management Action | Only acceptable with adequate controls | Commission Planning Committee |
| Critical | Urgent Management Action Required | Only acceptable with excellent controls | Commissioner |

| Safe Work Methods |
| --- |
| Job Steps | Potential Hazards | L | C | R | Controls / Work Methods 1. Eliminate 2. Substitute 3. Isolate 4. Engineer 5. Admin 6. PPE | Responsible Person/s for Monitor & Review | Residual Risk |
|  |  |  |  |  |  |  | L | C | R |
| Prior to entering a confined space | Insufficient planning for confined space entry | 4 | 5 | I 20 | Entry into a confined space is only to be permitted if a "Confined Space Entry Permit” and A Risk Assessment have been ratified for that particular confined space by the responsible Supervisor. All work activities to be performed in the confined space must be documented on the Confined Space Entry Permit and the Entry Permit must be displayed in a prominent position (outside the space) prior to confined space entry or works commencing. Controls required to ensure the safety of persons entering/working in the space must be identified on the Confined Space Entry Permit and implemented prior to confined space entry. Access to, and work performed in a confined space is only to be undertaken and supervised. Entry points to all confined spaces are to be signposted and secured against unauthorised entry by way of barricading or other suitable means of exclusion (i.e. signage indicating the presence of a confined space, and that entry is restricted to authorised personnel only). | Supervisor Workers | 2 | 5 | A 10 |
| Undertaking atmospheric monitoring | Faulty or uncelebrated gas detection unit | 3 | 3 | A 9 | A suitable gas detection unit must be selected and used for monitoring the atmospheric conditions that may exist in the confined space. Ensure that the gas detection unit has been calibrated in accordance with the manufacturers’ recommendations. A copy of the calibration certificate is to be kept on site. | Supervisor Workers | 2 | 3 | E 6 |
|  | Person not competent in use of gas detection unit | 3 | 3 | A 9 | Person(s) using the gas detection unit must be trained and competent in its operation. | Supervisor Workers | 2 | 3 | E 6 |
| Entering a confined space | Unauthorised access | 4 | 3 | A 12 | All persons entering the confined space must sign in and out (refer to the Confined Space Entry Permit. Entry or work in a confined space is not permitted unless entry has been authorised (and validated for the duration of the entry) by the supervisor. Training to be completed by all personnel entering the confined space | Supervisor Workers | 2 | 3 | E 6 |
|  | Not familiar with working in a confined space | 5 | 5 | I 25 | All personnel involved with the confined space (including planning) to have completed the required confined space training for entry into a confined space. Personnel who are assigned the testing of the confined spaces are to have been trained in the use of the gas tester and how to complete the testing of a confined space. | Supervisor Workers | 1 | 5 | E 5 |
|  | Change in conditions / environment | 4 | 4 | I 16 | If the confined space works environment changes, the Supervisor is to suspend work, restrict access to the area immediately, and notify the HSE advisor pending reassessment of the confined space. | Supervisor Workers | 2 | 4 | E 8 |
|  | Unsafe oxygen levels | 5 | 5 | I 25 | Air monitoring is to be undertaken prior to entry and throughout the period of entry to ensure that atmospheric conditions remain safe. | Supervisor Workers | 2 | 5 | A 10 |
|  | Insufficient ventilation | 5 | 5 | I 25 | The risk assessment conducted as part of the Confined Space Entry Permit must determine if mechanical (or induced) ventilation is required to remove fumes and/or dust etc. from the space. | Supervisor Workers | 2 | 5 | A 10 |
|  | Hazardous substance use | 3 | 3 | A 9 | Substances involved in the work procedures must be identified and authorised for use in the confined space. Hazardous substance / dangerous goods are to be used in accordance with the relevant SDS. | Supervisor Workers | 2 | 3 | E 6 |
|  | Fire / Explosion | 3 | 4 | A 12 | The risk assessment conducted as part of the Confined Space Entry Permit must identify any precautions involving hot work processes (i.e. welding, oxy-acetylene cutting). This will include blanking of pipework into the vessel, purging of the vessel with an inert gas and continuous atmospheric testing. If hot works are to be conducted a Hot Work Permit must be completed in accordance with SWMS 02 - Hot Work. Testing of confined spaces to ensure LEL and UEL limits are satisfactory. | Supervisor Workers | 2 | 4 | E 8 |
|  | Exposure to contaminants | 3 | 3 | A 9 | The risk assessment conducted as part of the Confined Space Entry Permit, must identify any personal protective equipment (i.e. self-contained breathing apparatus, respirators, gas monitors, communication devices, safety harness, safety goggles etc.) needed to perform work safely. If personal protective equipment is required it must be supplied to those persons involved prior to confined space entry along with instruction in its use and maintenance. | Supervisor Workers | 2 | 3 | E 6 |
|  | Insufficient emergency planning | 3 | 4 | A 12 | The risk assessment conducted as part of the Confined Space Entry Permit must identify emergency equipment and stand-by personnel necessary to rescue workers from the confined space and must be incorporated into any work procedures. All emergency equipment (i.e. rescue harnesses etc.) identified for the confined space works being performed is to be readily accessible to emergency personnel, suitably maintained and tested prior to use. At least one (1) stand-by person must be assigned to all confined space activities. | Supervisor Workers | 2 | 4 | E 8 |
|  | Insufficient communication | 3 | 3 | A 9 | A suitable means of communication is to be established to allow constant monitoring of those persons working in the confined space. | Supervisor Workers | 2 | 3 | E 6 |
| Completion of work in confined space | Failing to ensure all personnel have exited the confined space | 4 | 5 | I 20 | The Supervisor is to ensure that all personnel and equipment have been accounted for prior to restoring the confined space. | Supervisor Workers | 2 | 5 | A 10 |
|  | Failing to adequately secure the confined space | 4 | 5 | I 20 | After all personnel and equipment have been accounted for, the confined space is to be adequately secured to protect against unauthorised access. Suitable signage in accordance with AS1319 is also to be affixed to the confined space entry point (where relevant). | Supervisor Workers | 2 | 5 | A 10 |

Methods for monitoring and reviewing effectiveness of chosen control measures

Corruption and Crime Commission & Subcontracted Personnel: Supervisor: Ensure Confined Space Entry Permit is completed, entry personnel are competent and monitor the SWMS requirements on site using the Observation form Workers: Follow the procedure and report any hazards

| Developed & approved on site by: |
| --- |
| Name: | Position: | Date: |
|  | Manager / Supervisor |  |
|  | Workers Representative |  |

| Risk Assessment to Determine Lifting Requirements for High Risk Loads |
| --- |
| Item to be moved or Lifted | Manual Handling required / persons | Mechanical Aids required | Travel Distance | Work area requirements | Comments |

| I acknowledge that I have been trained in the SWMS listed above, the controls are clearly understood, my qualifications are current to undertake the activity, I will comply with the SWMS and I have been consulted and had the opportunity to input into the SWMS. |
| --- |
| Print Names | Position / Trade | Signature: | Date |

| Monitoring & Review of SWMS Use and Effectiveness |
| --- |
| Task Observation | 01 | 02 | 03 | 04 | 05 | 06 |
| Initial: |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |