| Department Details |
| --- |
| Location of Task: |  | Contact name and number: |  |
| Activity Description: | Performing hot work activities (for the purpose of this WMS, “hot work” includes grinding, welding, thermal or oxygen cutting or heating, and other related heat producing or spark producing operations). |
| Referenced SWMS: | SWMS 01; |
| Plant and Equipment Involved: | Hot work equipment and associated attachments, components etc. |
| PPE Required: (Tick as relevant) | Hard Hat | ( | Safety glasses / goggles | ( | Hearing Protection | ( | Fall Arrest Harness | ( | Other: | ( |
|  | Safety Boots | ( | Face Shield | ( | Gloves | ( | Respirator | ( | Hi Vis shirt/vest | ( |
| Maintenance / Prestart Checks Required: | Daily pre-use inspections of all hot work equipment and connections, attachments and fittings to check for wear, damage and condition before use. Inspection and maintenance in accordance with manufacturer recommendations |
| Certificates of Competency Required: | Nil |
| Training / Competencies Required: | Induction into this Safe Work Method Statement |
| Occupational Health, Safety or Environmental Legislation: | Occupational Health and Safety Act 1984 (WA) Occupational Health and Safety Regulations 1996 (WA) | Codes or Standards Applicable to the Works: | AS 1674 – Safety in welding and allied processes. AS 1558 Protective clothing for welders (except section 2.2) Health and Safety in Welding Advisory Standard, WTIA Technical Note 7. |

# Risk Matrix

| Perform a risk assessment for each hazard identified by: (i) Determining the consequences (refer Table 1); (ii) Determining the probability of the event occurring (refer Table 2); (iii) Apply the values obtained from Tables 1 & 2 to the Qualitative Risk Matrix (Table 3) to obtain the resultant Risk Score and Level. |
| --- |
| Table 1 – Consequence |  |
| Level Rating ASSESSMENT CRITERIA Injury or Disease Financial Loss (% of operational budget) Operational Efficiency Compliance Information and Evidence Reputation and Image 1 Insignificant No injuries or health effects Up to 0.025% Delay (up to 2 hours) in performance. All business objectives still achieved. Guidance required for compliance. Loss, unauthorised release or access to information resulting in an insignificant impact on operations and/or systems. Unsubstantiated Low impact Low or no media profile 2 Minor First aid treatment 0.025% - 0.15% Delay (2 hours – 1 day) in performance limiting full achievement of business objectives. Some minor, non-compliance issues. Loss, unauthorised release or access to information resulting in minor compromise of operations and/or systems. Substantiated Low impact Low media profile 3 Moderate Medical treatment 0.15% - 2% Delay (1 day – 1 week) in achievement of business objectives. Compliance or probity infringements. Loss, unauthorised release or access to information resulting in significant compromise of operations and/or systems. Substantiated Public embarrassment Moderate impact Moderate media profile 4 Major Permanent disability or disease 2% - 6% Delay (1 week – 1 month) with potential for non-achievement of major business objectives. Non-compliance resulting in penalties. Loss, unauthorised release or access to information resulting in substantial compromise of operations and/or systems. Substantiated Public embarrassment High impact High media profile Third party action 5 Catastrophic Death > 6% Delay >1 month. Non-achievement of major business objectives. Non-compliance resulting in criminal charges or loss of accreditation. Loss, unauthorised release or access to information resulting in the cancellation of an operation(s) and/ or total compromise of systems. Substantiated Public embarrassment Very high multiple impacts High widespread media profile Third party action Table 2 - Likelihood Level Descriptor Description Frequency 1 Rare The event may occur in exceptional circumstances. Has the event occurred during the last ten years? Is there more than a 5% chance of the event occurring? 2 Unlikely The event could occur at some time. Has the event occurred during the last five years? Is there more than a 10% chance of the event occurring? 3 Possible The event should occur at some time. If the event has occurred during the last five years has it occurred more than once? Is there more than a 25% chance of the event occurring? 4 Likely The event will probably occur in most circumstances. Has the event occurred during the past year? Is there more than a 50% chance of the event occurring? 5 Almost Certain The event is expected to occur in most circumstances. If the event has occurred during the past year has it occurred more than once? Is there more than a 95% chance of the event occurring? |  |
| Table 3 – Risk Level Consequence Likelihood 1 2 3 4 5 Rare Unlikely Possible Likely Almost Certain 1 Insignificant 1 2 3 4 5 2 Minor 2 4 6 8 10 3 Moderate 3 6 9 12 15 4 Major 4 8 12 16 20 5 Catastrophic 5 10 15 20 25 Table 4 - Level of Risk - Descriptor Low Risk Moderate Risk High Risk Critical Risk 1 - 4 5 - 8 9 -12 15 - 25 Table 5 - Control Rating Table Level Descriptor Description Detail E Excellent Doing more than what is reasonable under the circumstances. Controls fully in place and subject to continuous maintenance and monitoring. Protection systems are in place and continuously reviewed. Procedures are in place and regularly tested and reviewed. A Adequate Doing what is reasonable under the circumstances. Controls are in place and subject to periodic maintenance and monitoring. Protection systems are in place and are periodically reviewed. Procedures exist for given circumstances and are periodically tested and reviewed. I Inadequate Not doing some or all of the things that would be reasonable under the circumstances. Little or no action being taken. No protection systems exist or they have not been reviewed for some time. No formalised procedures exist. | Legend E: extreme risk; immediate reaction required (18-25) H: high risk; senior management attention needed (10-17) M: moderate risk; management responsibility must be specified (6-9) L: low risk; manage by routine procedures (1-5) |

# Table 6 - Risk Acceptance Table

| Level of Risk | Criteria for Acceptance of Risk | Authorised to accept |
| --- | --- | --- |
| Low | Acceptable | Acceptable with adequate controls | Risk Owner |
| Moderate | Acceptable with Monitoring | Acceptable with adequate controls | Manager |
| High | Acceptable with Management Action | Only acceptable with adequate controls | Commission Planning Committee |
| Critical | Urgent Management Action Required | Only acceptable with excellent controls | Commissioner |

| Safe Work Methods |
| --- |
| Job Steps | Potential Hazards | L | C | R | Controls / Work Methods 1. Eliminate 2. Substitute 3. Isolate 4. Engineer 5. Admin 6. PPE | Responsible Person/s for Monitor & Review | Residual Risk |
|  |  |  |  |  |  |  | L | C | R |
| Complete Hot Work Permit | Failing to complete hot work permit and identify hazards and /or suitable hot work controls | 3 | 4 | A 12 | Hot Work Permit to be completed prior to any hot work activities being undertaken outside the workshop. | Workers | 2 | 4 | E 8 |
| Pre-start checks | Failing to identify damaged or faulty equipment / connections / fittings | 3 | 4 | A 12 | Conduct a visual inspection of all hot work equipment and attachments to check for damage, wear etc, and withdraw from service / replace any identified faulty or damaged items of hot work equipment / attachments. | Supervisor Workers | 2 | 4 | E 8 |
| Undertaking hot work activities | Contact with hot objects | 3 | 3 | A 9 | All workers undertaking hot work activities are to be instructed in the safe use and specific precautions required with all apparatus and tasks performed, and are to be competent for the type of work to be performed. Personnel protective equipment must be worn when undertaking hot work activities. This may include: Welding mask / shield Leather gauntlets Leather aprons Safety footwear Respiratory protection Welding spats Hand protection Overalls or long sleeve shorts and trousers | Supervisor Workers | 2 | 3 | E 6 |
|  | Fire & explosion | 3 | 4 | A 12 | All bottles / cylinders, hoses and connections are to be checked to ensure they are connected correctly and ready for safe use prior to undertaking hot work activities. Suitable flashback arrestors are to be fitted to oxy-acetylene equipment on both hoses and cylinders. A fire extinguisher is to be provided in close proximity where hot work activities are to be carried out. Any debris and combustible materials are to be removed from the vicinity of the hot work area prior to the hot work commencing and good housekeeping practices ensured. Hot work activities are not to be performed in the vicinity of flammable or combustible agents. Gas cylinders shall be stored in a cool, dry place away from direct sunlight and other sources of heat. They must be secured while they are stored, moved and used on site. Cylinders are to be clearly marked to indicate the gas contained. Precautions are to be taken to minimise exposure and the potential effects of hazardous substances and to avoid fire and explosion hazards. Material Safety Data Sheets (MSDS) are to be followed relating to safe use, storage, labelling and personal protective equipment when using these substances. Gas cylinders are to be secured in an upright position to prevent them from falling | Supervisor Workers | 2 | 4 | E 8 |
|  | Inhalation of fumes / dust (working in a confined space) | 3 | 3 | A 9 | Only fully trained confined space personnel with documented methods of work, entry permits and air-monitoring procedures are to undertake hot work in confined spaces. All confined spaces work is to be undertaken in accordance with SWMS:12 Confined Spaces. Adequate ventilation (natural ventilation or mechanical dilution ventilation) suitable for the type of work is to be ensured whenever hot work activities are undertaken. Where ventilation is inadequate to fully protect a worker, respiratory protection is to be worn. Respiratory Protection: Protection must be assessed to be suitable for the fumes, gases, vapours or particulates being released. Particulate respirators (Class P2 filter) for thermal particulate / fumes and particulate in general;. Gas and vapour respirators for protection from ozone, nitrogen oxides and organic vapours. Airline respirators for welding work in confined spaces (AS 1715 & 1716). | Trained Confined Space Personnel Workers | 2 | 3 | E 6 |
|  | Inhalation of fumes / dust (normal work areas) | 3 | 3 | A 9 | Adequate ventilation (natural ventilation or mechanical dilution ventilation) suitable for the type of work is to be ensured whenever hot work activities are undertaken. Where ventilation is inadequate to fully protect a worker, respiratory protection is to be worn. Respiratory Protection: Protection must be assessed to be suitable for the fumes, gases, vapours or particulates being released. Particulate respirators (Class P2 filter) for thermal particulate / fumes and particulate in general;. Gas and vapour respirators for protection from ozone, nitrogen oxides and organic vapours. Airline respirators for welding work in confined spaces (AS 1715 & 1716). | Workers | 2 | 3 | E 6 |
|  | Arc flash / radiation exposure | 3 | 3 | A 9 | The work area is to be isolated to reduce the impact on persons working below or adjacent to the oxy-acetylene operations where they have the ability to affect other workers. Hazards associated with ultraviolet radiation must be controlled on site. This to be achieved by following, in order of priority, the following: Work areas are to be isolated, by translucent screens; Persons in the welding area are to wear appropriate personal protective equipment; Persons not carrying out welding activities are not to be permitted to enter an area through the use of adequate warning signs to warn of the hazards. | Workers Supervisor | 2 | 3 | E 6 |

Methods for monitoring and reviewing effectiveness of chosen control measures

Corruption and Crime Commission & Subcontracted Personnel: Supervisor: Ensure competent persons only perform hot work activities and monitor the activity. Workers: Follow the procedure and report any hazards

| Developed & approved on site by: |
| --- |
| Name: | Position: | Date: |
|  | Manager / Supervisor |  |
|  | Workers Representative |  |

| Risk Assessment to Determine Lifting Requirements for High Risk Loads |
| --- |
| Item to be moved or Lifted | Manual Handling required / persons | Mechanical Aids required | Travel Distance | Work area requirements | Comments |

| I acknowledge that I have been trained in the SWMS listed above, the controls are clearly understood, my qualifications are current to undertake the activity, I will comply with the SWMS and I have been consulted and had the opportunity to input into the SWMS. |
| --- |
| Print Names | Position / Trade | Signature: | Date |

| Monitoring & Review of SWMS Use and Effectiveness |
| --- |
| Task Observation | 01 | 02 | 03 | 04 | 05 | 06 |
| Initial: |  |  |  |  |  |  |
| Date: |  |  |  |  |  |  |